## Slide 1: Sensor based nitrate detection kit
Dr.S.Krishna kumar* and P.Kumaravel
*Associate Professor and Head
Department of Veterinary Public health and Epidemiology
Veterinary College and Research Institute, Udumalpet
epivetkrishna@gmail.com

## Slide 2: Preamble
Nitrate (NO3- ) is an ion . It readily dissolves in water and is an essential plant nutrient often applied to crops to help aid growth.
Nitrate - frequently contaminated in fodder, water and milk and blood.
Sources
sewage contamination
faculty natural farming
improper fertilizer management
addition of chemicals as preservatives
Nitrate poisoning methaemoglobin anoxia death.
Early diagnosis & prompt treatment better clinical outcome

## Slide 3: Current scenario
Kits at field level - purely qualitative.
Unable to detect the nitrate in quantitative level at farm gate
Immediate diagnosis and treatment - Better clinical outcome.
Currently available nitrate detection methods - time consuming and too far from farm gate

## Slide 4: Colour measurement Semi quantitative method
0.5% | 1.0 % | 1.0-2.0% | >2.0% | NEGATIVE

## Slide 5: Intervention.
Development of nitrate quantification system by sensor system
Electrical pulses equals to nitrate concentration by sensors.
Quantitative method
No chemicals

## Slide 6: Hand held Probe

## Slide 7: Mechanism
The Nitrate sensor contains a Permafil electrode containing nitrate ions inside a membrane.
Electrode will attract only nitrate in the solution
Measuring the electrical potential of attraction
The difference in potentials is raw mV value
This mV value is correlated to ion concentration
The sensor can determine the level of nitrate in the solution.

## Slide 8: Specifications
Sensor :Solid state ISE sensor
Measurement range : 0-30,000 mg/l
Accuracy :+/- 10% of reading
Samples : Blood, Urine, Milk and Fodder

## Slide 9: Out come
Real time results
Accurate
Low cost testing
On time treatment
Better clinical outcome

## Slide 10
Any suggestions
Any comments
Any questions
Thank you to all my co workers